## Slide 1
Model-measurement comparisons during Australian extreme bushfires: MUSICA and AQFx
Master of Philosophy (MPhil)
Samantha Lee1,
Supervisors: Clare Murphy2, Jason Evans1, Tim Raupach1
1. University of New South Wales, 2. University of Wollongong,

## Slide 2
The Context
In 2019 – 2020, south-east Australia faced one of the worst bushfire seasons in its recorded history:
Area burnt: 10.2 million hectares
Fatalities: 33
Buildings lost: 31,000 homes
Imagery provided by services from NASA's Global Imagery Browse Services (GIBS), part of NASA's Earth Science Data and Information System (ESDIS).
Canadell et al., 2021
Satellites estimates of forest area burnt in Australia

## Slide 3
Imagery provided by services from NASA's Global Imagery Browse Services (GIBS), part of NASA's Earth Science Data and Information System (ESDIS).
The Context
In 2019 – 2020, south-east Australia faced one of the worst bushfire seasons in its recorded history:
Area burnt: 10.2 million hectares
Fatalities: 33
Buildings lost: 31,000 homes
The Characterizing Organics and Aerosol Loading over Australia (COALA-2020) campaign measured atmospheric chemistry emissions from December 2019 to March 2020.
Most comprehensive smoke dataset for the region
Notes: Fire events are really hard to project in climate models, Current trajectory indicates conditions which increase the frequency and intensity of bushfires like this could increase under climate change

## Slide 4
Motivation
Reliable Modelling of Atmospheric Emissions
Future Climate Research
Emission Studies
Air Quality Management
Dissemination of Public Health Advice
Notes: There is an opportunity to compare the measurement of COALA to the outputs of some select atmospheric chemistry climate models and determine how well they projected the conditions surrounding this extreme smoke event.
This will help us understand how reliable they are for use for future climate research, emissions studies, air quality management and dissemination of public health advice

## Slide 5
Aims
Compare COALA-2020 measurements to the output of three atmospheric chemistry climate models
Determine how well they reproduce the chemical species concentrations in smoke plumes from extreme bushfires.
Present the results of the overall effectiveness of each model for each chemical species particular to the Australian context.

## Slide 6
COALA-2020 Measurement Data
Chemical Species measurements occurring from December 2019 to March 2020
Instruments Deployed in the AIRBOX:
PTR-ToF-MS
FTIR
3D sonic anemometer
AQMS (NSW DCCEEW)
Multi-angle absorption photometer
Notes: Held up by the 2020 eruption of the Taal Volcano

## Slide 7
PRT-TOF-MS | FTIR | Three-dimensional sonic anemometer | AQMS | Multi-angle absorption photometer
Methanol | Carbon dioxide | Wind speed | Humidity, relative | Black carbon, aerosol
Acetonitrile | Methane | Wind speed, maximum | Temperature, air | Aerosol absorption coefficient
Acetaldehyde | Carbon monoxide | Wind direction | Visibility, NEPH | 
Prop-2-enal | Nitrous oxide |  | Particulate matter, < 2.5 µm | 
Acetone | carbon dioxide |  | Particulate matter, < 10 µm | 
Isoprene |  |  | Ozone | 
Methacrolein + methyl vinyl ketone |  |  | Nitric oxide | 
Butan-2-one |  |  | Nitrogen dioxide | 
Benzene |  |  | Nitrogen oxides | 
Toluene |  |  | Sulfur dioxide | 
Sum C8H10 (Xylene) |  |  | HEIGHT above ground | 
Sum C9H12 |  |  | Wind speed | 
Monoterpenes |  |  | Wind direction | 
+ more |  |  | Wind direction, standard deviation | 
Instruments and Measured Species in COALA- 2020

## Slide 8
Chemical Species of Interest
Human Health Impact | Contributing to Atmospheric Reactions | Greenhouse Gas
Acetaldehyde | Isoprene | Methane
Carbon monoxide | Formic acid | 
Nitrogen dioxide | Nitric oxide | 
Sulfur dioxide |  | 
Ozone |  | 
Methanol |  | 
PM2.5 |  | 
PM10 |  | 

## Slide 9
The Models - AQFx
A regional atmospheric model that was developed as a tool to provide guidance to fire and land management agencies in Victoria for the minimization of population exposure to smoke from planned burns
9km x 9 km resolution
Average hourly concentrations
Inventories used:
State EPA inventories
Fuel layer map from AFDRS
EF derived from Pyrotron and FTIR experiments
Weather Modelling
Bureau of Meteorology ACCESS model
24h forecasts at 12:00
Regional Australian Model
Resolution
Model Data provided by Julie Noonan at the CSIRO, Australia
Notes: Replace and extend WACCM, CAM-Chem, WRF-CHEM
WRF-CMAQ used satellite of area burned and reports
AQFx uses hotspot as well as reports from ground
MUSICA uses satellite data and the FINN emissions inventory

## Slide 10
Reisen, F et al, 2024

## Slide 11
The Models – CESM MUSICA
100 km x 100 km resolution
Average hourly concentrations
Inventories used:
QFED CO2 x FINN emission ratios for fire
CAMS-GLOB-ANT version 5.1
MEGAN 2.1
Dust by Leung et al 2024 scheme
Weather Modelling
Meteorology is nudged towards MERRA2 reanalysis
Global model with regional refinement capability
Resolution
The Multi-Scale Infrastructure for Chemistry and Aerosols model, under development at NSF NCAR for simulating of large-scale atmospheric phenomena, while resolving chemistry at emission and exposure relevant scales.
https://www2.acom.ucar.edu/sections/multi-scale-infrastructure-chemistry-modeling-musica
Model Data provided by Rebecca Buchholz at NSF National Center for Atmospheric Research
Notes: Replace and extend WACCM, CAM-Chem, WRF-CHEM
WRF-CMAQ used satellite of area burned and reports
AQFx uses hotspot as well as reports from ground
MUSICA uses satellite data and the FINN emissions inventory

## Slide 12
Preliminary Results
Ozone measured in COALA-2020 compared to the outputs of AQFx and MUSICA models

## Slide 13
Boxplot for Ozone

## Slide 14
Quantitative Comparison of Ozone

## Slide 15
Quantitative Comparison of Ozone
Regulatory exceedance level 115 µg/m3

## Slide 16
Exceedance Criteria of Ozone
Green shading indicates where the model was correct
Red shading indicates where the model was incorrect
True Positive
False Negative
False Positive
True Negative
True Positive
False Negative
False Positive
True Negative

## Slide 17
Exceedance Criteria of Ozone
Green shading indicates where the model was correct
Red shading indicates where the model was incorrect
True Positive
False Negative
False Positive
True Negative
True Positive
False Negative
False Positive
True Negative
Highly unbalanced, which skews some metrics

## Slide 18
F1-score
Harmonic mean of precision and recall.
= 2 x (Precision x Recall) / (Precision + Recall)
Exceedance Criteria of Ozone
Accuracy
How often are the model predictions correct?
= (True Positive + True Negatives) / Total Predictions
Recall
How many of the true positive instances does the model successfully capture?
= True Positives / (True Positives + False Negatives)
Precision
How often is a positive prediction correct?
= True Positives / (True Positives + False Positives)

## Slide 19
Metric | AQFx | MUSICA
Accuracy | 0.92 | 0.89
Precision | 0.60 | 0.48
Recall | 0.69 | 0.78
F1 Score | 0.64 | 0.60
Exceedance Criteria of Ozone

## Slide 20
Preliminary Results
PM 2.5 measured in COALA-2020 compared to the outputs of AQFx and MUSICA models

## Slide 21
Boxplot for PM 2.5

## Slide 22
Quantitative Comparison of PM 2.5
Regulatory exceedance level 16.75 µg/m3

## Slide 23
Exceedance Criteria of PM 2.5
Green shading indicates where the model was correct
Red shading indicates where the model was incorrect
True Positive
False Negative
False Positive
True Negative
True Positive
False Negative
False Positive
True Negative
127
532
355
0
374
361
108
171
Confusion Matrix Heatmap for PM 2.5 in AQFx
Confusion Matrix Heatmap for PM 2.5 in MUSICA

## Slide 24
Exceedance Criteria of PM 2.5
Green shading indicates where the model was correct
Red shading indicates where the model was incorrect
True Positive
False Negative
False Positive
True Negative
True Positive
False Negative
False Positive
True Negative
127
532
355
0
374
361
171
Confusion Matrix Heatmap for PM 2.5 in AQFx
Confusion Matrix Heatmap for PM 2.5 in MUSICA
This time, no false positives
108

## Slide 25
Metric | AQFx | MUSICA
Accuracy | 0.65 | 0.72
Precision | 1.0 | 0.69
Recall | 0.26 | 0.78
F1 Score | 0.42 | 0.73
Exceedance Criteria of PM 2.5

## Slide 26
Summary
Using COALA-2020 measurements as a point of comparison, the results for ozone and PM2.5 for AQFx and MUSICA were compared.
The AQFx most accurately reproduces ozone levels, while MUSICA co-varies with COALA-2020 measurements but tends to overestimate high concentration levels consistently.
PM 2.5 simulations were generally worse, AQFx values are very low so no false positives lead to a high precision, but MUSICA performs best in all other fields
In-person visit on 4-15 August 2025
sam.lee2@unsw.edu.au

## Slide 27
Thank you to Julie Noonan (CSIRO Australia) and Rebecca Buchholz (NSF National Center for Atmospheric Research) for providing data for this work
References
Canadell, J. G., Meyer, C. P. (Mick), Cook, G. D., Dowdy, A., Briggs, P. R., Knauer, J., et al. (2021). Multi-decadal increase of forest burned area in Australia is linked to climate change. Nature Communications, 12(1), 6921. https://doi.org/10.1038/s41467-021-27225-4
Filkov, A. I., Ngo, T., Matthews, S., Telfer, S., & Penman, T. D. (2020). Impact of Australia’s catastrophic 2019/20 bushfire season on communities and environment. Retrospective analysis and current trends. Journal of Safety Science and Resilience, 1(1), 44–56. https://doi.org/10.1016/j.jnlssr.2020.06.009
Reisen, F. (2024). AQFx- a national smoke forecasting system: From emissions to forewarning. Conference Presentation for 2024 CASANZ AirTalks, accessed 06 June 2025.
Image from https://wwf.org.au/what-we-do/australian-bushfires/, accessed 31 May 2025.
Imagery provided by services from NASA's Global Imagery Browse Services (GIBS), part of NASA's Earth Science Data and Information System (ESDIS), https://worldview.earthdata.nasa.gov
Leung, D. M., Kok, J. F., Li, L., Mahowald, N. M., Lawrence, D. M., Tilmes, S., et al. (2024). A new process-based and scale-aware desert dust emission scheme for global climate models – Part II: Evaluation in the Community Earth System Model version 2 (CESM2). Atmospheric Chemistry and Physics, 24(4), 2287–2318. https://doi.org/10.5194/acp-24-2287-2024
https://www2.acom.ucar.edu/sections/multi-scale-infrastructure-chemistry-modeling-musica
Thank you!

## Slide 28
Air Quality Monitoring Station
https://www.environment.nsw.gov.au/topics/air/air-quality-basics/how-and-why-we-monitor-air-pollution
Filter deposition, then measured by microbalance or Beta Radiation Attenuation